## Slide 1
Dimensionality Reduction
and Measurement Reconstruction
for Time-Lapse Fiber-Optic Sensing
Misael M. Morales,
Carlos Torres-Verdín, and Michael J. Pyrcz
The University of Texas at Austin

## Slide 2: Table of Contents
2
Introduction and Motivation
Fiber-Optic Sensing
Experimental System
Technical Challenges for In Situ Monitoring
Dimensionality Reduction Techniques
Results and Discussion
Conclusions and Future Work

## Slide 3: Introduction and Motivation
Digital revolution allows better subsurface profiling
  Data science techniques help processing and interpretation
3
Fiber optics allows for reliable, cost-effective, and detailed monitoring
  Applications in geothermal, CCUS, hydraulic fracturing, EOR, etc.
   Large volumes of data
Tsuji et. al. (2021)
Maio et. al. (2010)

## Slide 4: Fiber-Optic Sensing
Cost-effective and high-resolution alternative for downhole monitoring
Naldrett et. al. (2018)
Distributed Acoustic Sensing (DAS)
  Measurement of axial strain rate along the fiber
Advantages:
  No moving parts
  No downhole electronics
  Deployed throughout wellbore
4

## Slide 5: Experimental System: Flow Loop Design
50-meter flow loop with internal and external tubing:
  Background + 4 perforations flowing O/G/W
  Fiber optic cable in annulus recording DAS & DTS
1
2
3
4
F.O. cable
5,504 measurements
13 minutes @ 10 kHz
Injection points
Injection 1:
O – 250
W – 250
G – 8,333.3
Injection 2:
O – 250
W – 100
G – 8,333.3
Injection 3:
O – 0
W – 0
G – 0
Injection 4:
O – 250
W – 250
G – 8,333.3
Background:
O – 3,000
W – 0
G- 100,000
In collaboration with:
5

## Slide 6: Experimental System: DAS Data Acquisition
In collaboration with:
6
  Time [s] vs. Distance [m]
  Amplitudes
  Injection points shown as 
Time-lapse DAS response along the flowloop
100 Gb of DAS data in “.h5”
  Compress to 1.56 Gb “.pkl”
  5504 m  200 m
  13 minutes  7 minutes

## Slide 7: Technical Challenges for In Situ Monitoring
Data from Fiber-Optic sensing can be hard to use
  Sensitivity to noise
  Sensor reliability
  Event detection in real time
  Data volume: 200 Mbps interrogator, 1 Mbps cloud  0.5% CR
Data-driven techniques allow for improved processing and analysis
  Reduced-dimensional space for efficient compression, interpretation, and reconstruction
7

## Slide 8: Dimensionality Reduction Techniques: Overview
Modeling and analysis in reduced-dimensional space:
  Compressed representation of main features,
  Accelerate processing and interpretation
  Reconstruct data from salient features,
8
z
Original
Data
Reconstructed Data

## Slide 9: Dimensionality Reduction Techniques: Methods and Metrics
SVD, PCA, FFT, DWT, and Deep Learning AutoEncoders
  Compared at different compression ratios:
  Error metrics:
    Mean squared error:
    Structural similarity index measure:
    Peak signal-to-noise ratio:
9

## Slide 10: Dimensionality Reduction Techniques: SVD
Singular Value Decomposition (SVD)
  Decompose data matrix, , into 3 components:
  Only retain leading terms, removing redundancy and preserving most important features for reconstruction:
  relates to the energy conserved in the decomposition
From Wikipedia, SVD
10

## Slide 11: Dimensionality Reduction Techniques: SVD
11
MSE: 1.61e-4
SSIM: 97.37%
PSNR: 43.96 dB
10% CR
MSE: 2.85e-4
SSIM: 94.68%
PSNR: 41.90 dB
5% CR
0.5% CR
MSE: 1.45e-3
SSIM: 79.40%
PSNR: 34.40 dB

## Slide 12: Dimensionality Reduction Techniques: PCA
Principal Component Analysis (PCA)
  One of the most classical dimensionality reduction techniques
  Eigenvectors of the covariance matrix
  Maximize variance explained in each eigendirection:
  where is the normalized covariance matrix
  Limitations: linear transform, covariance calculation, outlier sensitivity
12

## Slide 13: Dimensionality Reduction Techniques: PCA
13
MSE: 8.06e-5
SSIM: 97.91%
PSNR: 46.96 dB
10% CR
MSE: 1.55e-4
SSIM: 95.49%
PSNR: 44.12 dB
5% CR
0.5% CR
MSE: 1.40e-3
SSIM: 79.54%
PSNR: 34.54 dB

## Slide 14: Dimensionality Reduction Techniques: FFT
Fast Fourier Transform (FFT)
  Uses generic basis of sines/cosines from eigenvectors of data matrix
  Retains a range of frequency components in the data by shifting from time-space to frequency-wavenumber domain
  where
14

## Slide 15: Dimensionality Reduction Techniques: FFT
15
MSE: 3.26e-4
SSIM: 95.01%
PSNR: 40.89 dB
10% CR
MSE: 3.79e-4
SSIM: 94.24%
PSNR: 40.24 dB
5% CR
0.5% CR
MSE: 1.39e-2
SSIM: 77.15%
PSNR: 34.59 dB

## Slide 16: Dimensionality Reduction Techniques: DWT
Discrete Wavelet Transform (DWT)
  Uses generic basis of sines/cosines from eigenvectors of data matrix
  Exploits multiresolution information for spatiotemporal analysis by adaptive filtering of frequency bands for localized information
  where and are coefficients, is the scaling function,
  and is the wavelet function (Daubechies type 2)
16

## Slide 17: Dimensionality Reduction Techniques: DWT
17
MSE: 6.89e-5
SSIM: 98.17%
PSNR: 47.64 dB
10% CR
MSE: 1.28e-4
SSIM: 96.71%
PSNR: 44.95 dB
5% CR
0.5% CR
MSE: 4.98e-4
SSIM: 88.02%
PSNR: 39.05 dB

## Slide 18: Dimensionality Reduction Techniques: DL-AE
Deep Learning AutoEncoders
  Recent advanced in computing power allow for powerful models for advanced dimensionality reduction and data reconstruction
  Variety of styles and architectures can be designed:
    Fully-Connected Neural Networks (FCNN)
    Convolutional Neural Networks (CNN)
    Variational, Recurrent, Adversarial, etc. …
18

## Slide 19: Dimensionality Reduction Techniques: DL-AE
Convolutional NN
Fully-Connected NN
19
Activation = PReLU
Optimizer = Adam
Loss = MSE
Epochs = 50
# Params: 102,820
# Params: 171,677
Notes: NVIDIA M6000

## Slide 20: Dimensionality Reduction Techniques: DL-AE
20
MSE: 1.52e-2
SSIM: 70.03%
PSNR: 34.18 dB
CNN – 5% CR
FCNN – 5% CR
MSE: 1.97e-2
SSIM: 65.45%
PSNR: 27.32 dB

## Slide 21: Results and Discussion: Error Metrics
Comparison of error metrics for dimensionality reduction techniques
Technique | Computing Time | Latent Dimension | MSE [] | SSIM [%] | PSNR [dB]
SVD | 6m 54s | 5% | 2.85-4 | 94.68 | 41.90
PCA | 7m 8s | 5% | 1.55e-4 | 95.49 | 44.12
FFT | 7m 20s | 5% | 3.79e-4 | 94.24 | 40.24
DWT | 6m 28s | 5% | 1.28e-4 | 96.71 | 44.95
DL-AE FCNN | 5m 14s | 5% | 1.97e-2 | 65.45 | 27.32
DL-AE CNN | 12m 16s | 5% | 1.52e-2 | 70.03 | 34.18
21

## Slide 22: Results and Discussion: Reconstruction Efficiency
22
Comparison of reconstructions at 5% compression ratio

## Slide 23: Results and Discussion: Latent Space Interpretation
PCA and SVD: may not be best-suited for time series
  Do not represent all physics in the dynamical system
FFT and DWT: best exploit time signals but generic basis are not tailored to physics in the data
  Leading methods for image/video processing
Deep Learning AutoEncoders:
  Require expertise in design and training but incorporate all physics and dynamics in the time series data
23

## Slide 24: Conclusions and Future Work
Classical techniques have up to 95% SSIM at 5% CR
Deep learning techniques have up to 70% SSIM at 5% C.R.
  Further tuning and training required to improve models
In the future:
  Use flowrates and Distributed Temperature Sensing data in latent vector
  Event detection and classification in latent space
  Noise suppression and enhanced data compression and reconstruction
24

## Slide 25: Acknowledgements
25

## Slide 26: References
26
[1] Mateeva, A., Lopez, J., Chalenski, D., Tatanova, M., Zwartjes, P., Yang, Z., Bakku, S., de Vos, K., and Potters, H., 2017, “4D DAS VSP as a tool for frequent seismic monitoring in deep water”, Leading Edge, Tulsa, Oklahoma, v. 36, n. 12, p. 995-1000.
[2] Zwartjes, P., Mateeva, A., Chalenski, D., Duan, Y., Kiyashchenko, D., and Lopez, J., 2018, “Frequent, multi-well, stand-alone 3D DAS VSP for low-cost reservoir monitoring in deepwater”, SEG International Exposition and Annual Meeting, Anaheim, California, October.
[3] Luo, B., Lellouch, A., Jin, G., Biondi, B., and Simmons, J., 2021, “Seismic inversion of shale reservoir properties using microseismic-induced guided waves recorded by distributed acoustic sensing”, Geophysics, v. 86, n. 4, p. R383-R397.
[4] Liu, F., Huff, O., Luo, B., Jin, G., and Simmons, J., 2022, “Convolutional neural network-based classification of microseismic events originating in a stimulated reservoir from distributed acoustic sensing data”, Geophysical Prospecting, v. 70, n. 5, p. 904-920.
[5] Feng, Q., and Li, Y., 2022, “Denoising deep learning network based on singular spectrum analysis – DAS seismic denoising with multichannel SVDDCNN”, IEEE Transactions on Geoscience and Remote Sensing, v. 60, p. 1-11.
[6] Binder, G., and Tura, A., 2020, “Convolutional neural network for automated microseismic detection in downhole distributed acoustic sensing data and comparison to a surface geophone array”, Geophysical Prospecting, v. 68, n. 9, p. 2770-2782.
[7] Zhong, T., Cheng, M., Lu, S., Dong, X., and Li, Y., 2022, “RCEN: a deep-learning-based background noise suppression method for DAS-VSP records”, IEEE Geoscience and Remote Sensing Letters, v. 19, p. 1-5.
[8] Tsuji, T., Ikeda, T., Matsuura, R., Mukumoto, K., Lawrens Hutapea, F., Kimura, T., Yamaoka, K., and Shinohara, M., 2021, “Continuous monitoring system for safe managements of CO2 storage and geothermal reservoirs”, Scientific Reports, v. 11, n. 1, p. 19120-19120.
[9] Maio, V., Gribik, A., Patterson, M., and Boardman, R., 2010, “Nuclear-integrated oil sands recovery via steam-assisted gravity drainage”, Idaho National Lab Reports, n. 23843, p. 8-12.
[10] Naldrett, G., Cerrahoglu, C., and Mahue, V., 2018, “Production monitoring using next-generation distributed sensing systems”, Petrophysics, v. 59, n. 4, p. 496-510.

## Slide 27
Thank You
Q & A

## Slide 28
Backup Slides

## Slide 29: Backup Slides
29
where is the original data matrix,
is the reconstruction matrix,
and and are small stability constants

## Slide 30: Backup Slides
30
ReLU PReLU
Rectified Linear Unit Parametric Rectified Linear Unit
Where is a learned array with the same shape as ,
and is initialized as zeros (ReLU)