## Slide 1
A Deep Learning-Based Dual Latent Space Method for the Estimation of Physical Flow Properties from Fiber-Optic Measurements
Misael M. Morales, Carlos Torres-Verdín, and Michael Pyrcz
The University of Texas at Austin
August 14th-15th 2023
23rd Annual Formation Evaluation Research Consortium Meeting (2023)

## Slide 2: Table of Contents
Introduction and Motivation
Fiber-Optic Sensing
Experimental System
Dimensionality Reduction Techniques
Dual Latent Space Method
Results and Discussion
Conclusions and Future Work
2

## Slide 3: Introduction and Motivation
3
Digital revolution enables better subsurface profiling
  Data science techniques help processing and interpretation
Fiber optics enables reliable, cost-effective, and detailed monitoring
  Applications in geothermal, CCUS, hydraulic fracturing, EOR, etc.
   Large volumes of data

## Slide 4: Fiber-Optic Sensing: Pros and Cons
4
Distributed Acoustic (DAS) and Temperature (DTS) Sensing
  DAS: continuous measurement of axial strain along the fiber
  DTS: continuous measurement of temperature profile along the fiber

## Slide 5: Fiber-Optic Sensing
5
Cost-effective and high-resolution alternative for downhole monitoring
Distributed Acoustic (DAS) and Temperature (DTS) Sensing
Data-driven dimensionality reduction for improved processing and analysis
Advantages:
  No moving parts
  No downhole electronics
  Deployed throughout wellbore
Challenges:
  Sensitivity to noise
  Sensor reliability
  Real-time event detection
  Data volume

## Slide 6: Experimental Design
6
50-meter flow loop with internal and external tubing:
  Background + 4 perforations flowing O/G/W/Sandstone
  Fiber optic cable in annulus recording DAS and DTS
In collaboration with:
1
2
3
4
F.O. cable
5,504 measurements
13 minutes, 10 kHz
Injection points
Injection 1:
O – 250
W – 250
G – 8,333.3
S – 0
Injection 2:
O – 250
W – 100
G – 8,333.3
S – 0
Injection 3:
O – 0
W – 0
G – 0
S – 0
Injection 4:
O – 250
W – 250
G – 8,333.3
S – 10
Background:
O – 3,000
W – 0
G – 100,000
S – 0
Distance [m]
Time samples
Time samples

## Slide 7: Experimental Design: Data Processing
7
Data Processing
Flow Rates {O,G,W,S} Normalized to
Injection location
Captured into a single data frame,

## Slide 8: Dimensionality Reduction Techniques: Overview
8
Modeling and analysis in reduced-dimensional space:
  Compressed representation of main features,
  Accelerate processing and interpretation
  Reconstruct data from salient features,
z
Original
Data
Reconstructed Data

## Slide 9: Dimensionality Reduction Techniques: Findings
9
Comparison of reconstructions at 5% compression ratio
Distance [m]
Time samples

## Slide 10: Dimensionality Reduction Techniques: Comparison
10
Comparison of error metrics for dimensionality reduction techniques
Technique | Computing Time | Latent Dimension | MSE [] | SSIM [%] | PSNR [dB]
SVD | 6m 54s | 5% | 2.85-4 | 94.68 | 41.90
PCA | 7m 8s | 5% | 1.55e-4 | 95.49 | 44.12
FFT | 7m 20s | 5% | 3.79e-4 | 94.24 | 40.24
DWT | 6m 28s | 5% | 1.28e-4 | 96.71 | 44.95
DL-AE FCNN | 5m 14s | 5% | 1.97e-2 | 65.45 | 27.32
DL-AE CNN | 12m 16s | 5% | 1.52e-2 | 70.03 | 34.18

## Slide 11: Dimensionality Reduction Techniques: Summary
11
PCA and SVD: not best-suited for time series analysis
  Do not represent all physics in the dynamical system
FFT and DWT: best exploit time signals but generic basis not tailored to physics in the data
  Leading methods for image/video processing
Deep Learning AutoEncoders:
  Require expertise in design and training but incorporate all physics and dynamics in the time series data

## Slide 12: Dual Latent Space Method: Architecture
12
Latent space:
Reconstruction:
Rates
and
Locations
Dual latent:
Estimation:

## Slide 13: Dual Latent Space Method: U-net AutoEncoders
13
Latin Hypercube Sampling
Resample DAS using LHS to the same frequency as DTS
Does not require much training data to accurately predict parameters
Both the DAS U-net and DTS U-net have identical architectures

## Slide 14: Dual Latent Space Method: Training Performance
14
DAS U-net:
  45,333 parameters
  1 minute, 16 sec
  MSE =
  SSIM = 87.70%
  PSNR = 25.25
 DAS training performance
DTS training performance 
DTS U-net:
  45,333 parameters
  1 minutes, 12 sec
  MSE =
  SSIM = 94.35%
  PSNR = 25.93
True
Predicted
Abs. Error
Latent Space

## Slide 15: Dual Latent Space Method: Parameter Estimation
15
Use the pre-trained AutoEncoder networks to:
Compress DAS and DTS into latent space
Concatenate into a single dual latent space,
Use these features to predict:
  Injection location
  Relative flow rates

## Slide 16: Dual Latent Space Method: Transfer Learning
16
A highly-overdetermined inverse problem!
can be any (multi-output) scikit-learn regressor  e.g., Ridge
MSE= | SSIM = 100%
MSE= | SSIM = 99.99%
Transfer Learning (Testing) with new Experiment
Rates
and
Locations

## Slide 17: Results and Discussion
Dual Latent Space Model captures hidden physics and dynamics in the spatio-temporal data
  Tailored (learned) parameters to extract main features from the data
Flow Rate and Injection Location predictions in 0.6 seconds from dual (pre-processed) DAS and DTS measurements
  Accuracy over 99%, even for transfer learning process
17

## Slide 18: Conclusions and Future Work
18
Dual Latent Space Method proves fast and accurate to predict physical flow parameters in fiber-optic measurements
Future work:
  Compare performance using only 1 AutoEncoder network (no dual latent space)
  Quantify the uncertainty in estimation by adding random noise
  Additional dimensionality reduction for to tackle overdetermined inversion
  Calculate the trade-off in prediction by varying latent-space size

## Slide 19: Acknowledgments
19

## Slide 20: References
20
[1] Mateeva, A., Lopez, J., Chalenski, D., Tatanova, M., Zwartjes, P., Yang, Z., Bakku, S., de Vos, K., and Potters, H., 2017, “4D DAS VSP as a tool for frequent seismic monitoring in deep water”, Leading Edge, Tulsa, Oklahoma, v. 36, n. 12, p. 995-1000.
[2] Zwartjes, P., Mateeva, A., Chalenski, D., Duan, Y., Kiyashchenko, D., and Lopez, J., 2018, “Frequent, multi-well, stand-alone 3D DAS VSP for low-cost reservoir monitoring in deepwater”, SEG International Exposition and Annual Meeting, Anaheim, California, October.
[3] Luo, B., Lellouch, A., Jin, G., Biondi, B., and Simmons, J., 2021, “Seismic inversion of shale reservoir properties using microseismic-induced guided waves recorded by distributed acoustic sensing”, Geophysics, v. 86, n. 4, p. R383-R397.
[4] Liu, F., Huff, O., Luo, B., Jin, G., and Simmons, J., 2022, “Convolutional neural network-based classification of microseismic events originating in a stimulated reservoir from distributed acoustic sensing data”, Geophysical Prospecting, v. 70, n. 5, p. 904-920.
[5] Feng, Q., and Li, Y., 2022, “Denoising deep learning network based on singular spectrum analysis – DAS seismic denoising with multichannel SVDDCNN”, IEEE Transactions on Geoscience and Remote Sensing, v. 60, p. 1-11.
[6] Binder, G., and Tura, A., 2020, “Convolutional neural network for automated microseismic detection in downhole distributed acoustic sensing data and comparison to a surface geophone array”, Geophysical Prospecting, v. 68, n. 9, p. 2770-2782.
[7] Zhong, T., Cheng, M., Lu, S., Dong, X., and Li, Y., 2022, “RCEN: a deep-learning-based background noise suppression method for DAS-VSP records”, IEEE Geoscience and Remote Sensing Letters, v. 19, p. 1-5.
[8] Tsuji, T., Ikeda, T., Matsuura, R., Mukumoto, K., Lawrens Hutapea, F., Kimura, T., Yamaoka, K., and Shinohara, M., 2021, “Continuous monitoring system for safe managements of CO2 storage and geothermal reservoirs”, Scientific Reports, v. 11, n. 1, p. 19120-19120.
[9] Maio, V., Gribik, A., Patterson, M., and Boardman, R., 2010, “Nuclear-integrated oil sands recovery via steam-assisted gravity drainage”, Idaho National Lab Reports, n. 23843, p. 8-12.
[10] Naldrett, G., Cerrahoglu, C., and Mahue, V., 2018, “Production monitoring using next-generation distributed sensing systems”, Petrophysics, v. 59, n. 4, p. 496-510.

## Slide 21
Thank You
Q & A
August 14th-15th 2023
23rd Annual Formation Evaluation Research Consortium Meeting (2023)

## Slide 22
Backup Slides
A Deep Learning-based Dual Latent Space Method for the Estimation of Physical Flow Properties from Fiber-Optic Measurements
August 14th-15th 2023
23rd Annual Formation Evaluation Research Consortium Meeting (2023)

## Slide 23: Backup Slides
23
where is the original data matrix,
is the reconstruction matrix,
and and are small stability constants

## Slide 24: Backup Slides
24
ReLU PReLU
Rectified Linear Unit Parametric Rectified Linear Unit
Where is a learned array with the same shape as ,
and is initialized as zeros (ReLU)